## Slide 1: NodeMCU - Installing ESP32 Board in the Arduino IDE
Step 1: Installing or Updating the Arduino IDE
Step 2: Installing the USB-to-Serial Bridge Driver
https://www.silabs.com/products/development-tools/software/usb-to-uart-bridge-vcp-drivers
http://www.wch-ic.com/downloads/CH341SER_ZIP.html
https://raw.githubusercontent.com/espressif/arduino-esp32/gh-pages/package_esp32_index.json

## Slide 2: Use CaseStudy Environmental monitoring using NodeMCU (ESP32) with DHT22 and Thingspeak Cloud Computing

## Slide 3: NodeMCU - Installing ESP32 Board in the Arduino IDE
Step 1: Installing or Updating the Arduino IDE
Step 2: Installing the USB-to-Serial Bridge Driver
https://www.silabs.com/products/development-tools/software/usb-to-uart-bridge-vcp-drivers
http://www.wch-ic.com/downloads/CH341SER_ZIP.html
Step 3: Installing the ESP32 Arduino Core
https://raw.githubusercontent.com/espressif/arduino-esp32/gh-pages/package_esp32_index.json

## Slide 4: NodeMCU - Installing ESP32 Board in the Arduino IDE
Step 3: Installing the ESP32 Arduino Core
https://raw.githubusercontent.com/espressif/arduino-esp32/gh-pages/package_esp32_index.json

## Slide 5: NodeMCU - Installing ESP32 Board in the Arduino IDE
Step 3: Installing the ESP32 Arduino Core
https://raw.githubusercontent.com/espressif/arduino-esp32/gh-pages/package_esp32_index.json

## Slide 6: NodeMCU - Installing ESP32 Board in the Arduino IDE
Step 3: Installing the ESP32 Arduino Core
Environmental monitoring using NodeMCU (ESP32) with DHT22
Environmental monitoring using NodeMCU (ESP32) with DHT22

## Slide 7: NodeMCU - Installing ESP32 Board in the Arduino IDE
Step 3: Installing the ESP32 Arduino Core
a. Install Arduino ESP32
b. ESP32

## Slide 8: NodeMCU
Courtesy:
https://www.studiopieters.nl/esp32-pinout/

## Slide 9: NodeMCU
15 ADC channels | 15 channels of 12-bit SAR ADC with selectable ranges of 0-1V, 0-1.4V, 0-2V, or 0-4V
2 UART interfaces | 2 UART interfaces with flow control and IrDA support
25 PWM outputs | 25 PWM pins to control things like motor speed or LED brightness
2 DAC channels | Two 8-bit DACs to generate true analog voltages
SPI, I2C and I2S interface | Three SPI and one I2C interfaces for connecting various sensors and peripherals, as well as two I2S interfaces for adding sound to your project
9 Touch Pads | 9 GPIOs with capacitive touch sensing
ESP32 Peripherals and I/O
48 GPIO pins in total, only 25 of them are broken out to the pin headers on both sides of the development board. These pins can be assigned a variety of peripheral duties, including:
Courtesy:
https://www.studiopieters.nl/esp32-pinout/

## Slide 10: NodeMCU – DHT 11 interfacing
Courtesy: Lab@602 AB3

## Slide 11: NodeMCU

## Slide 12: NodeMCU

## Slide 13: NodeMCU (Environmental Program)
#include <ESP8266WiFi.h>
#include <DHT.h>
#include <ThingSpeak.h>
DHT dht(D5, DHT11);
WiFiClient client;
const char *ssid = "Rahul";
const char *pass = "12345678";
long myChannelNumber = 2400352;
const char myWriteAPIKey[] = "DT6UNP5Q36ARTV4U";
Wifi connection Since Simulation
No need for representing the
Wifi Name as well as WIFI Password
ThingSpeak Configuration www.thingspeak.com
APIKey:
Need to be represented in programming as well as the Thingspeak for sending the data from hardware to the cloud server thingspeak

## Slide 14: NodeMCU (Environmental Program)
void setup() {
// put your setup code here, to run once:
Serial.begin(115200);
WiFi.begin(ssid, pass);
while(WiFi.status() != WL_CONNECTED)
{
delay(200);
Serial.print("..");
}
Serial.println();
Serial.println("NodeMCU is connected!");
Serial.println(WiFi.localIP());
dht.begin();
ThingSpeak.begin(client);
}
DHT11 Library (as discussed in previous experiment

## Slide 15: NodeMCU (Environmental Program)
void loop() {
// put your main code here, to run repeatedly:
float h = dht.readHumidity();
float t = dht.readTemperature();
Serial.println("Temperature: " + (String) t);
Serial.println("Humidity: " + (String) h);
ThingSpeak.writeField(myChannelNumber, 1, t, myWriteAPIKey);
ThingSpeak.writeField(myChannelNumber, 2, h, myWriteAPIKey);
delay(10);
}
Applicable only for real time implmentation
Thingspeak Library
Arduino IDE -> Tools -> Manage Libraries -> Type Thingspeak and install the library

## Slide 16: NodeMCU (Environmental Program)
Parameters:
Humidity
Temperature
Are the both fields or variables to transfer the data from the hardware to the Thingspeak cloud for data visualization

## Slide 17: ThingSpeak Configuration for ESP32

## Slide 18: ThingSpeak

## Slide 19: ThingSpeak Configuration for ESP32
Channel Settings
Percentage complete: Calculated based on data entered into the various fields of a channel. Enter the name, description, location, URL, video, and tags to complete your channel.
Channel Name: Enter a unique name for the ThingSpeak channel.
Description: Enter a description of the ThingSpeak channel.
Field#: Check the box to enable the field, and enter a field name. Each ThingSpeak channel can have up to 8 fields.
Metadata: Enter information about channel data, including JSON, XML, or CSV data.
Tags: Enter keywords that identify the channel. Separate tags with commas.
Link to External Site: If you have a website that contains information about your ThingSpeak channel, specify the URL.
Show Channel Location:
  Latitude: Specify the latitude position in decimal degrees. For example, the latitude of the city of London is 51.5072.
  Longitude: Specify the longitude position in decimal degrees. For example, the longitude of the city of London is -0.1275.
  Elevation: Specify the elevation position meters. For example, the elevation of the city of London is 35.052.
Video URL: If you have a YouTube™ or Vimeo® video that displays your channel information, specify the full path of the video URL.
Link to GitHub: If you store your ThingSpeak code on GitHub®, specify the GitHub repository URL.
Using the Channel
You can get data into a channel from a device, website, or another ThingsSpeak channel. You can then visualize data and transform it using ThingSpeak Apps.
See Get Started with ThingSpeak" for an example of measuring dew point from a weather station that acquires data from an Arduino® device.

## Slide 20: ThingSpeak Configuration for ESP32

## Slide 21: ThingSpeak Configuration for ESP32

## Slide 22: ThingSpeak Configuration for ESP32
Save the Channel

## Slide 23: ThingSpeak Configuration for ESP32
Reconfiguring Channel
Different Visualization
Note down the Write API Key

## Slide 24: ThingSpeak Configuration for ESP32
Write API Key – Data transfer from Hardware to Thingspeak